## Slide 1
IMPACT OF COOLING CHANNEL SHAPE ON THE PERFORMANCE OF HOLLOW HAIRPIN WINDINGS
Multiphysics analysis and multi-objective channel shape optimization for direct oil-cooled hairpin windings
Hüseyin Tayyer Canseven
Department of Electrical Engineering, LUT University, Finland
Motivation
Traction motors: higher speed and frequency
Hairpin windings = industry standard
AC losses → severe local hot spots
Water jacket: long thermal path
Direct oil cooling
Oil flows inside each conductor
Heat extracted at the source
Hot spots suppressed
+277 % continuous current
Reference machine
Power / speed | 300 kW / 2000 rpm
Slots × layers | 48 × 4
Conductor | 6 × 4 mm
Current / frequency | 350 A, 266.7 Hz
Coolant | Oil, 65 °C, 10 L/min
Flow regime | Laminar
Can the channel be shaped freely for cooling?
Electromagnetic analysis
2D FEA: 350 A rms, 266.7 Hz
Current crowds at the periphery
Channel sits in the “dead zone”
Chart: 
| Layer 1 | Layer 2 | Layer 3 | Layer 4
Solid | 2002 | 800.2 | 273.5 | 32.5
Round | 1988.3 | 794.1 | 271.7 | 32.8
Rectangular | 1992.7 | 796.7 | 272.3 | 32.4
Channel-shape optimization
Bigger channel: more surface, less copper
Smaller channel: steep pressure drop
Temperature vs. pumping power compete
128 FE samples → surrogate → GA
Wall and opening ≥ 0.75 mm
Shape | Optimal size | Peak T | Pumping
Circular | Ø 0.75 mm | 127.4 °C | 34.8 W
Elliptical | 4.5 × 0.75 mm | 89.3 °C | 2.98 W
Rectangular | 4.5 × 0.75 mm | 78.8 °C | 1.92 W
Conclusions
Channel centre is EM “dead”: < 0.25 %
Shape it purely for cooling
Rectangle > ellipse ≫ circle
Round → rectangular: −10 °C peak
Optimum: 78.8 °C at 1.92 W
Next: manufacturing + motorette test
LABORATORY OF ELECTRICAL DRIVES TECHNOLOGY
Contact: Hüseyin T. Canseven (huseyin.canseven@lut.fi)
Ilya Petrov (ilya.petrov@lut.fi)
(a) solid (b) round (c) rectangular
AC loss per layer (W)
Optimal designs: (a) circular (b) rectangular (c) elliptical